## Slide 1
By
Annick Carnino
(former Director of IAEA Division of Nuclear Installations Safety)
PIME, February 13- 15, 2012

## Slide 2
Part I
Why Having Safety Standards

## Slide 3
Harmonization of safety to higher levels
Revision processes for new knowledge and experience feedback
References for Conventions
References for peer safety reviews
Basis for Legislations and Regulations in countries starting nuclear programmes

## Slide 4
Statute of IAEA
« …to establish or adopt …standards of safety for the protection of health and minimization of danger to life and property »
« and to provide for the application of these standards »

## Slide 5
Part II
IAEA Safety Standards

## Slide 6
Safety Standards Hierarchy
Safety Guides
Safety Requirements
Safety Fundamentals
Reference for a High Level of Nuclear Safety

## Slide 7
Safety Fundamental
    A must for every installation or activity
Safety Requirements
    Functional conditions required for safety
    Stable - but periodic review and revision if necessary
Safety Guides
    Guidance to fulfill the requirements
    User-friendly and up-to-date practical guidance
    representing good/best practices

## Slide 8
Fundamental Safety Principles
Principle 1: Responsibility for Safety
Principle 2: Role of Government
Principle 3: Leadership and Management for safety
Principle 4: Justification of facilities and activities
Principle 5: Optimization of protection
Principle 6: Limitation of risk to individuals
Principle 7: Protection of present and future generations
Principle 8: Prevention of accidents
Principle 9: Emergency preparedness and response
Principle 10: Protective actions to reduce existing of unregulated radiation risk

## Slide 10
OBJECTIVE
1.8. The objective of this publication is to define requirements for
establishing, implementing, assessing and continually improving a management
system that integrates safety, health, environmental, security, quality and
economic elements to ensure that safety is properly taken into account in all
the activities of an organization.
1.9. The main objective of the requirements for the management system is to
ensure, by considering the implications of all actions not within separate
management systems but with regard to safety as a whole, that safety is not
compromised.
Example on Safety Management

## Slide 12
Safety Analysis Methodologies

## Slide 13
Levels of Defence-In-Depth
Levels of Defence-in-depth | Objective | Essential means for achieving the objective
Level 1 | Prevention of abnormal operation and failures | Conservative design and high quality in construction and operation
Level 2 | Control of abnormal operation and detection of failures | Control, limiting and protection systems and systems and other surveillance features
Level 3 | Control of accidents within the design basis | Engineered safety features and accident procedures
Level 4 | Control of severe plant conditions, including prevention of accident progression and mitigation of the consequences of severe accidents | Complementary measures and accident management
Level 5 | Mitigation of radiological consequences of significant releases of radioactive materials | Off-site emergency response

## Slide 14
Part II
International Nuclear Safety Convention

## Slide 15
Obligations based on the first version of the safety fundamentals
Objectives:
to achieve and maintain a high level of nuclear safety worldwide..;
to protect individuals, society and the environment from harmful effect of ionizing radiation…;
to prevent accidents with radiological consequences and to mitigate such consequences should they occur.

## Slide 16
The Convention applies to “the safety of nuclear installations” (civil and land-based)
Each Contracting Party shall:
- ensure that the safety of nuclear installations is reviewed as soon as possible..;
- ensure that all reasonably practical improvements are made to upgrade the safety of the nuclear installation..;
- shut down the nuclear installation as soon as practically possible, if such upgrading cannot be achieved…

## Slide 18
•61 of the 72 Contracting Parties participated
•8 CP did not submit a national report and 11 did not participate
•Special statement on Fukushima was made
•A special meeting was decided for next year on reviewing and sharing the lessons learned and on actions taken by CPs

## Slide 19
Nuclear power plant design against external events;
Off site response to emergency situations (e.g. station blackout);
Emergency management and preparedness following worst case accident scenarios;
Safety consideration for operation of multi-units at the same Nuclear Power Plant site;
Cooling of spent fuel storage in severe accident scenarios;
Training of Nuclear Power Plant operators for severe accident scenarios;
Radiological monitoring following Nuclear Power Plant accident involving radiological release;
Public protection emergency actions;
Communications in emergency situations.

## Slide 20
Part IV
Safety Review Services

## Slide 21
Preparatory meeting one year before
Designation of IAEA team leader and selection of the « peer experts » from different countries
On site review starting with team bonding and training,standards to be used
Every day discussion of the findings and recommendations, suggestions and presentation to the management
First report given to the installation managers and presentation to the personnel (exit meeting in presence of Regulator)
Two years later on site review of the recommendations implemented

## Slide 22
Safety Review Services based on IAEA Safety Standards
Concepts
Site evaluation
Construction
Pre-decommissioning
Decommissioning
Operation
Commissioning
Safety Assessment

## Slide 23
Regulatory Framework and Activities
  IRRS – Integrated Regulatory Review Service
Operational Safety
  OSART – Operational Safety Review Team
  SEDO – Safety Evaluation of Fuel Cycle Facilities During Operation
  SCART – Safety Culture Assessment Review Team
Notes: <number>

## Slide 24
Research Reactors
  INSARR – Integrated Safety Assessment of Research Reactors
Engineering and Technical Safety
  Safety Assessment Services – Engineering/Safety Assessment Review Services

## Slide 25
Member States asked the IAEA
to address issues related to nuclear safety, emergency preparedness and response and radiation protection of people and the environment, as well as the international legal framework.
to strengthen nuclear Safety Standards; to systematically review the safety of all nuclear power plants, including by expanding the IAEA's programme of expert peer reviews; to enhance the effectiveness of national nuclear regulatory bodies and ensure their independence; to strengthen the global emergency preparedness and response system; and to expand the Agency's role in receiving and disseminating information.